## Slide 1: Dynamixel SDK
ODROID Application

## Slide 2: Contents
CONTENTS
Environment
  H/W Setting
  S/W Configuration
  To do Demo
About Dynamixel SDK
  Protocol
  Packet
  Use
Demo Examples
  Lists
  Demo & Codes
Structure (API Reference)
  Folder
  Class
  Methods

## Slide 3: Environment

## Slide 4: Environment
1. H/W Settings
ODROID XU4
Dynamixel PRO
µSD Card
HDMI A-A Type Cable
(Metal shielded)
x 2
4P Cables (Molex)
x 4
5V/4A US Plug Power Supply
24V Power Supply
x 1
Power Cables
USB Hub
USB2Dynamixel
µSD-SD Adapter

## Slide 5: Environment
1. H/W Settings
Dynamixels
USB2Dynamixel
ODROID
HDMI
5V4A PWR
24 V PWR
ID 1 / ID 2
Baudrate : 1M
µSD Card
- for examples

## Slide 6: Environment
1. H/W Settings
/dev/ttyUSB0
/dev/ttyUSB1
ID : 1
ID : 2
- for MultiPort example on Linux

## Slide 7: Environment
1. H/W Settings
Download “RoboPlus”:
en.robotis.com → Support → Download → RoboPlus v*.exe
Choose one
- Dynamixel setting

## Slide 8: Environment
1. H/W Settings
- Dynamixel setting
RS485
Windows
Desktop

## Slide 9: Environment
1. H/W Settings
1. Click Dynamiel Wizard
1
2
3
2. Select the port connected with USB2DXL (check this in device manager)
3. Connect
- Dynamixel setting

## Slide 10: Environment
1. H/W Settings
1. Choose baudrate which you want to use to scan Dynamixels
2. Select DXL 2.0
3. Start searching
1
3
2
4
5
4. Choose Dynamixel that you want to edit its setting
5. Modify as: 1st DXL : ID = 1 / BaudRate = 3
2nd DXL : ID = 2 / BaudRate = 3
- Dynamixel setting

## Slide 11: Environment
1. H/W Settings
- ODROID OS setting
1
1. Download ODROID OS image (*.img.xz file)
Ubuntu 15.XX : ubuntu mate
Ubuntu 14.XX : Lubuntu
Unzip *.img.xz file with 7-zip
→ extract *.img file
D/L | http://odroid.com/dokuwiki/doku.php?id=en:xu3_release_linux_ubuntu

## Slide 12: Environment
1. H/W Settings
1
1. Download Win32 Disk Imager for ODROID
Exract and install it
- ODROID OS setting
D/L | http://dn.odroid.com/DiskImager_ODROID/

## Slide 13: Environment
1. H/W Settings
Win XP, Win 7 users : See following at
http://com.odroid.com/sigong/blog/blog_list.php?bid=144
- ODROID OS setting

## Slide 14: Environment
1. H/W Settings
Linux users : See following at
http://com.odroid.com/sigong/blog/blog_list.php?bid=130
- ODROID OS setting

## Slide 15: Environment
1. H/W Settings
2. Choose *.img file to write on the μSD
3. Open *.img file
4. Select μSD Drive
3
5. Write
2
4
5
1
1. Put into Desktop through SD Adapter
- ODROID OS setting

## Slide 16: Environment
1. H/W Settings
- ODROID OS setting

## Slide 17: Environment
2. S/W Configuration
- Booting

## Slide 18: Environment
2. S/W Configuration
Press “Log In” and keep going
- Booting

## Slide 19: Environment
2. S/W Configuration
- Booting

## Slide 20: Environment
2. S/W Configuration
If the system suspends, unlock it by typing Password : odroid
- Booting

## Slide 21: Environment
2. S/W Configuration
1. Copy SDK file to Desktop
1
2
2. Application
→ System Tools
→ Mate Terminal
3
3. Play demos with Terminal
- Booting

## Slide 22: Environment
2. S/W Configuration
Source Download : DynamixelSDK_vX.Y.zip
https://github.com/ROBOTIS-GIT
C++ : GNU g++
Build Tool
Build-essential → make
Compiler
C : GNU gcc (Source is now being prepared…)

## Slide 23: Environment
3. To do Demo
1. Type as shown below, and press enter
$ sudo su
$ [sudo] password for odroid: odroid
2. Compile the SDK source
$ cd Desktop/DynamixelSDK_vX.Y/c++/src
$ make install
(If the file already exists, type: $ make reinstall)
3. Compile the example source
$ cd ../example/Protocol1.0/[example_sourcefile_name]
$ make
$ ./[example_name]
(If the file already exists, type: $ make clean and then make)
4. Execute the example
then, something makes happen in Dynamixels!

## Slide 24: Environment
3. To do Demo
ex) ReadWrite
Open the Terminal

## Slide 25: Environment
3. To do Demo
ex) ReadWrite
- See connected devices
1.
2. Check USB2Dynamixel
are recognized by the
controller as: ttyUSB0
$ ls /dev
2
1

## Slide 26: Environment
3. To do Demo
ex) ReadWrite
Type $ sudo su, then input P/W : [sudo] password for odroid: odroid

## Slide 27: Environment
3. To do Demo
ex) ReadWrite
Type # cd/Desktop/DynamixelSDK_vX.Y/c++/src/ and press Enter
Type # make reinstall and press Enter

## Slide 28: Environment
3. To do Demo
ex) ReadWrite
Type # cd ../example/Protocol2.0/ReadWrite/ and press Enter
Type # make and press Enter

## Slide 29: Environment
3. To do Demo
ex) ReadWrite
Type # ./ReadWrite and press Enter

## Slide 30: Environment
3. To do Demo
ex) ReadWrite
Press Enter again, and then the data appears to the terminal
Press Enter until you want to quit

## Slide 31: Environment
3. To do Demo
ex) ReadWrite
Press Esc and Enter to quit

## Slide 32: About Dynamixel SDK

## Slide 33: About Dynamixel SDK
Protocol
Dynamixel Protocol: a communication rule needed for Dynamixel control
Controller
Dynamixel
Protocol 1.0 : Dynamixel AX series / DX series / RX series / MX series
Protocol 2.0(*) : Dynamixel PRO(**), XL
Instruction Packet
Status Packet
(*) Purpose: for better accuracy of signal transmission/reception
(**) Dynamixel PRO: Dynamixel series used in Manipulator and Thormang lineup
“Rotate through 180 degrees!”
“Failed!”
“Done!”

## Slide 34: About Dynamixel SDK
2. Packet Architecture of Protocol 2.0
ID
Instruction Packet
Packet
Length
Instruction
Parameters
Header
Reserved (0x00)
# 1
# N
WRITE:
“Change”
READ:
“Let me know”
‘Goal position’ value
’Present position’ &value
Target Dynamixel
~
…
…
For checking
Packet error
CRC

## Slide 35: About Dynamixel SDK
2. Packet Architecture of Protocol 2.0
ID
Status Packet
Packet
Length
Instruction
(Status Packet)
Parameters
CRC
Header
Reserved (0x00)
Error
# 1
# N
STATUS:
“Here is my reply”
‘Transmit Success’
or
‘Transmit Failed’
value = ’Present position’
Target Dynamixel
~
…
For checking
Packet error
Dynamixel
error

## Slide 36: About Dynamixel SDK
3. Use
SDK API
Platform
PortHandler
PacketHandler
Model number
ID
Instruction
Parameter
Transmit
Dynamixel
Instruction
Present
position
No data
Receive
Instr. Packet
Status Packet
ID
Instruction
Parameter
CRC
Header
Length
ID
Parameter
CRC
Header
Length
Error
ID & Parameter

## Slide 37: Example

## Slide 38: Examples
1. Example List
Examples for Protocol 2.0 – Dynamixel PRO
Instructions
Ping
Read
Write
SyncRead
SyncWrite
BulkRead
BulkWrite
Reboot
FactoryReset
ReadWrite
Sync ReadWrite
Bulk ReadWrite
Examples
MultiPort
Indirect Address
Ping
BroadcastPing
Reboot
FactoryReset
Examples | Contents
Ping | Get DXL model number
BroadcastPing | Scan connected DXL
ReadWrite | Position control
MultiPort | Use two ports
SyncReadWrite | Access multi DXLs
BulkReadWrite | Access multi DXL, ADDR
IndirectAddress | Use Indirect Address
Reboot | Reboot DXL
FactoryReset | Reset all DXL settings

## Slide 39: Examples
2. Demo & Codes
- Shared settings
PortHandler *portHandler = (PortHandler*)PortHandler::GetPortHandler(DEVICE_NAME);
portHandler->OpenPort()
portHandler->SetBaudRate(BAUDRATE)
PacketHandler *packetHandler = PacketHandler::GetPacketHandler(PROTOCOL_VERSION);
: portHandler gets methods and members of PortHandlerLinux or PortHandlerWindows, and sets the DEVICE_NAME.
: portHandler opens and gets the handle of selected port.
: portHandler retries to open the selected port with selected BAUDRATE.
: packetHandler gets methods and members of Protocol1PacketHandler or Protocol2PacketHandler by PROTOCOL_VERSION.
portHandler->ClosePort()
: portHandler closes selected port.

## Slide 40: Examples
2. Demo & Codes
- ReadWrite : a Dynamixel rotates

## Slide 41: Examples
2. Demo & Codes
- ReadWrite : a Dynamixel rotates
#include ”dynamixel_sdk/DynamixelSDK.h”
#define DXL_ID 1
#define BAUDRATE 1000000
#define PROTOCOL_VERSION 2.0
#define DEVICE_NAME ”/dev/ttyUSB0”
#define ADDR_PRO_TORQUE_ENABLE 562
#define ADDR_PRO_GOAL_POSITION 596
#define ADDR_PRO_PRESENT_POSITION 611
#define ADDR_PRO_MOVING 610
// To handle the Dynamixel, include dynamixel_sdk/Dynamixel.h header file
// ID Number of the Dynamixel
// The communication baudrate btw contoroller and Dynamixel
// Protocol Version for making packet
// Device name for take a communication throught its port
// Control table address of TORQUE ENABLE
// Control table address of GOAL POSITION
// Control table address of MOVING status
// Control table address of PRESENT POSITION
continue to the next page...
/* defines */
/* Headers */

## Slide 42: Examples
2. Demo & Codes
- ReadWrite : a Dynamixel rotates
PortHandler *portHandler = (PortHandler*)PortHandler::GetPortHandler(DEVICE_NAME);
int dxl_goal_position[2] = {-150000, 150000};
UINT8_T dxl_torque_enable = 1;
UINT8_T dxl_torque_disable = 0;
UINT16_T dxl_present_position = 0;
UINT8_T dxl_moving = 0;
int main(){
// Dynamixel goal position value
// Dynamixel torque enable value
// Dynamixel torque disable value
// Dynamixel moving status value
// Dynamixel present position value
int index = 0;
// Index for rotation direction
continue to the next page...
UINT8_T dxl_error = 0;
// Dynamixel error
/* Variables */
/* Handlers */
PacketHandler *packetHandler = PacketHandler::GetPacketHandler(PROTOCOL_VERSION);

## Slide 43: Examples
2. Demo & Codes
packetHandler->Write4ByteTxRx(portHandler, DXL_ID, ADDR_GOAL_POSITION, dxl_goal_position[index], &dxl_error);
- ReadWrite : a Dynamixel rotates
packetHandler->Read4ByteTxRx(portHandler, DXL_ID, ADDR_PRESENT_POSITION, &dxl_present_position, &dxl_error);
packetHandler->Read1ByteTxRx(portHandler, DXL_ID, ADDR_MOVING, &dxl_moving, &dxl_error);
do{ // Do-While loop for Read present position
}while(dxl_moving == 1)
printf(“[ID:%03d] Present Position = %05d”, DXL_ID, dxl_present_position);
While(1){ // While loop for Write goal position
if(_getch() == 0x1b) break; // Press ESC and ENTER to quit
}
if( index == 1 ) index = 1;
else index = 0;
packetHandler->Write1ByteTxRx(portHandler, DXL_ID, ADDR_TORQUE_ENABLE, dxl_torque_enable, &dxl_error);
portHandler->OpenPort()
portHandler->SetBaudRate(BAUDRATE)
packetHandler->Write1ByteTxRx(portHandler, DXL_ID, ADDR_TORQUE_ENABLE, dxl_torque_disable, &dxl_error);
portHandler->ClosePort()
/* Body */

## Slide 44: Examples
2. Demo & Codes
- ReadWrite : a Dynamixel rotates
: is needed to make packets and send it through the port.
Explanation
#include ”dynamixel_sdk/DynamixelSDK.h”
: The example uses DXL_ID #1 at 1M baudrate. It makes Protocol 2.0 packet and sends through the port ”/dev/ttyUSB0”.
#define DXL_ID 1
#define BAUDRATE 1000000
#define PROTOCOL_VERSION 2.0
#define DEVICE_NAME ”/dev/ttyUSB0”
: defines addresses of the control table, which are used by Read and Write data.
#define ADDR_PRO_TORQUE_ENABLE 562
#define ADDR_PRO_GOAL_POSITION 596
#define ADDR_PRO_PRESENT_POSITION 611
#define ADDR_PRO_MOVING 610
[Replace below codes to the DEFINES]
[Replace below codes to the HEADERS]

## Slide 45: Examples
2. Demo & Codes
- ReadWrite : a Dynamixel rotates
: dxl_error keeps the error got from Dynamixel. The index indicates the rotation direction of Dynamixel. The dxl_goal_position points out where the Dynamixel should be rotated to. The value of dxl_torque_enable and dxl_torque_disable mean that torque ON and OFF, each. The dxl_moving shows the moving state of the Dynamixel. The dxl_present_position stores the present position value of Dynamixel.
Explanation
: initialize the handlers of the port and the packet.
int dxl_goal_position[2] = {-150000, 150000};
UINT8_T dxl_torque_enable = 1;
UINT8_T dxl_torque_disable = 0;
UINT32_T dxl_present_position = 0;
UINT8_T dxl_moving = 0;
int index = 0;
UINT8_T dxl_error = 0;
PortHandler *portHandler = (PortHandler*)PortHandler::GetPortHandler(DEVICE_NAME);
PacketHandler *packetHandler = PacketHandler::GetPacketHandler(PROTOCOL_VERSION);
[Replace below codes to the HANDLERS]
[Replace below codes to the VARIABLES]

## Slide 46: Examples
2. Demo & Codes
- ReadWrite : a Dynamixel rotates
: opens the port and sets the port baudrate.
Explanation
portHandler->SetBaudRate(BAUDRATE)
portHandler->OpenPort()
: enables the torque of the Dynamixel.
packetHandler->Write1ByteTxRx(portHandler, DXL_ID, ADDR_TORQUE_ENABLE, dxl_torque_enable, &dxl_error);
: starts to write either of the dxl_goal_positions and repeats Read the dxl_present_position and dxl_moving status until the Dynamixel stops moving. After that, the index indicates another dxl_goal_position by changing its value.
packetHandler->Write4ByteTxRx(portHandler, DXL_ID, ADDR_GOAL_POSITION, dxl_goal_position[index], &dxl_error);
packetHandler->Read4ByteTxRx(portHandler, DXL_ID, ADDR_PRESENT_POSITION, &dxl_present_position, &dxl_error);
packetHandler->Read1ByteTxRx(portHandler, DXL_ID, ADDR_MOVING, &dxl_moving, &dxl_error);
do{
}while(dxl_moving == 1);
printf(“[ID:%03d] Present Position = %05d”, DXL_ID, dxl_present_position);
While(1){
if(_getch() == 0x1b) break;
}
if( index == 1 ) index = 1;
else index = 0;
[Replace below codes to the BODY]

## Slide 47: Examples
2. Demo & Codes
- ReadWrite : a Dynamixel rotates
packetHandler->Write1ByteTxRx(portHandler, DXL_ID, ADDR_TORQUE_ENABLE, dxl_torque_disable, &dxl_error);
portHandler->ClosePort()
: closes the port.
: disables the torque of the Dynamixel.
Explanation

## Slide 48: Examples
2. Demo & Codes
- Ping : shows model number of Dynamixel

## Slide 49: Examples
2. Demo & Codes
packetHandler->Ping(portHandler, DXL_ID, &dxl_model_number, &dxl_error);
: tries to Ping the DXL_ID and gets dxl_model_number. Then, it shows the model number of the Dynamixel.
- Ping : shows model number of Dynamixel
Explanation
: dxl_error keeps the error got from Dynamixel. dxl_model_number stores the model number of Dynamixel.
UINT8_T dxl_error = 0;
[Replace below codes to the VARIABLES]
UINT16_T dxl_model_number = 0;
[Replace below codes to the BODY]
printf(”[ID:%03d] DXL model number : %d\n”, DXL_ID, dxl_model_number);

## Slide 50: Examples
2. Demo & Codes
- BroadcastPing : shows the list of connected Dynamixels

## Slide 51: Examples
packetHandler->BroadcastPing(portHandler, vec);
: tries to BroadcastPing all Dynamixels and gets the list of connected Dynamixels. Then, it shows the ID of connect Dynamixels
printf(”[ID:%03d]\n”, vec.at(i));
UINT8_T dxl_error = 0;
: dxl_error keeps the error got from Dynamixel. ‘vec’ stores the list of connected Dynamixels
2. Demo & Codes
- BroadcastPing : shows the list of connected Dynamixels
Explanation
[Replace below codes to the BODY]
#include <vector>
: Try to BroadcastPing all Dynamixels and gets the list of connected Dynamixels.
[Replace below codes to the VARIABLES]
[Replace below codes to the HEADERS]
std::vector<UINT8_T> vec;
for(int i = 0; i < (int)vec.size(); i++)

## Slide 52: Examples
2. Demo & Codes
- MultiPort : two Dynamixels rotate using two ports

## Slide 53: Examples
packetHandler->Write4ByteTxRx(portHandler1, DXL1_ID, ADDR_GOAL_POSITION, dxl_goal_position, &dxl_error);
packetHandler->Read4ByteTxRx(portHandler1, DXL1_ID, ADDR_PRESENT_POSITION, &dxl_present_position1, &dxl_error);
packetHandler->Write4ByteTxRx(portHandler2, DXL2_ID, ADDR_GOAL_POSITION, dxl_goal_position, &dxl_error);
packetHandler->Read4ByteTxRx(portHandler2, DXL2_ID, ADDR_PRESENT_POSITION, &dxl_present_position2, &dxl_error);
: Write dxl_goal_positions to each Dynamixels through two ports.
: Read dxl_present_position on each Dynamixels through two ports.
2. Demo & Codes
- MultiPort : two Dynamixels rotate using two ports
Explanation

## Slide 54: Examples
2. Demo & Codes
- SyncReadWrite : writes same data of two Dynamixels

## Slide 55: Examples
#define ADDR_PRO_TORQUE_ENABLE 562
2. Demo & Codes
- SyncReadWrite : writes same data of two Dynamixels
#define ADDR_PRO_GOAL_POSITION 596
#define ADDR_PRO_PRESENT_POSITION 611
#define LEN_PRO_TORQUE_ENABLE 1
: defines byte length for each items.
#define LEN_PRO_GOAL_POSITION 4
#define LEN_PRO_PRESENT_POSITION 4
#define DXL1_ID 1
#define DXL2_ID 2
#define BAUDRATE 1000000
[Replace below codes to the DEFINES]
: The example uses DXL_ID #1 and DXL_ID #2 at 1M baudrate. It makes Protocol 2.0 packet and sends through the port ”/dev/ttyUSB0”. STOP_MOVING_MARGIN is for deciding whether the Dynamixel moves or not
: defines addresses of the control table, which are used by Sync Read and Write data.
#define PROTOCOL_VERSION 2.0
#define STOP_MOVING_MARGIN 20
Explanation

## Slide 56: Examples
2. Demo & Codes
- SyncReadWrite : writes same data of two Dynamixels
: dxl_error keeps the error got from Dynamixel. The index indicates the rotation direction of Dynamixel. The dxl_goal_position points out where the Dynamixel should be rotated to. The value of dxl_torque_enable and dxl_torque_disable mean that torque ON and OFF, each. The dxl_goal_position will be allocated into param_goal_position byte array. The dxl_present_position1 and dxl_present_position2 store the present position value of Dynamixels.
int dxl_goal_position[2] = {-150000, 150000};
UINT8_T dxl_torque_enable = 1;
UINT8_T dxl_torque_disable = 0;
UINT32_T dxl_present_position1, dxl_present_position2 = 0;
UINT8_T param_goal_position[4];
int index = 0;
UINT8_T dxl_error = 0;
[Replace below codes to the VARIABLES]
: initialize the handlers of the port and the packet. Then initializes groupSyncWrite instance using two handlers above.
PortHandler *portHandler = (PortHandler*)PortHandler::GetPortHandler(DEVICE_NAME);
PacketHandler *packetHandler = PacketHandler::GetPacketHandler(PROTOCOL_VERSION);
[Replace below codes to the HANDLERS]
GroupSyncWrite groupSyncWrite(portHandler, packetHandler, ADDR_GOAL_POSITION, LEN_GOAL_POSITION);
GroupSyncRead groupSyncRead(portHandler, packetHandler, ADDR_PRESENT_POSITION, LEN_PRESENT_POSITION);

## Slide 57: Examples
groupSyncWrite.TxPacket();
groupSyncWrite.ClearParam();
groupSyncWrite.AddParam(DXL1_ID, param_goal_position);
groupSyncWrite.AddParam(DXL2_ID, param_goal_position);
: AddParameter param_goal_position to groupSyncWrite parameter storage
: Transmits the packet
: ClearParameter of groupSyncWrite parameter storage.
param_goal_position[0] = DXL_LOBYTE(DXL_LOWORD(dxl_goal_position));
param_goal_position[1] = DXL_HIBYTE(DXL_LOWORD(dxl_goal_position));
param_goal_position[2] = DXL_LOBYTE(DXL_HIWORD(dxl_goal_position));
param_goal_position[3] = DXL_HIBYTE(DXL_HIWORD(dxl_goal_position));
: allocates dxl_goal_position into the byte array
2. Demo & Codes
- SyncReadWrite : writes same data of two Dynamixels
: starts to write either of the dxl_goal_positions and repeats Read the dxl_present_position and dxl_moving status until the Dynamixel stops moving. After that, the index indicates another dxl_goal_position by changing its value.
packetHandler->Write4ByteTxRx(portHandler, DXL_ID, ADDR_GOAL_POSITION, dxl_goal_position[index], &dxl_error);
packetHandler->Read4ByteTxRx(portHandler, DXL_ID, ADDR_PRESENT_POSITION, &dxl_present_position, &dxl_error);
packetHandler->Read1ByteTxRx(portHandler, DXL_ID, ADDR_MOVING, &dxl_moving, &dxl_error);
do{
}while(dxl_moving == 1);
printf(“[ID:%03d] Present Position = %05d”, DXL_ID, dxl_present_position);
While(1){
if(_getch() == 0x1b) break;
}
if( index == 1 ) index = 1;
else index = 0;
[Replace below codes to the BODY]
groupSyncRead.AddParam(DXL1_ID);
groupSyncRead.AddParam(DXL2_ID);
: AddParameter storage for Dynamixel’s present position value
: enables the torque of the Dynamixel.
packetHandler->Write1ByteTxRx(portHandler, DXL_ID, ADDR_TORQUE_ENABLE, dxl_torque_enable, &dxl_error);

## Slide 58: Examples
groupSyncRead.TxRxPacket();
groupSyncRead.GetData(DXL1_ID, ADDR_PRESENT_POSITION, &dxl_present_position);
groupSyncRead.GetData(DXL2_ID, ADDR_PRESENT_POSITION, &dxl_present_position);
: Transmits and receives the packet.
: GetData of dxl_present_positions
groupSyncRead.ClearParam();
: ClearParameter of groupSyncRead parameter storage.
2. Demo & Codes
- SyncReadWrite : writes same data of two Dynamixels
packetHandler->Write1ByteTxRx(portHandler, DXL_ID, ADDR_TORQUE_ENABLE, dxl_torque_disable, &dxl_error);
: disables the torque of the Dynamixel.

## Slide 59: Examples
2. Demo & Codes
- BulkReadWrite : writes different data of two Dynamixels

## Slide 60: Examples
#define ADDR_PRO_TORQUE_ENABLE 562
2. Demo & Codes
#define ADDR_PRO_LED_RED 563
#define ADDR_PRO_GOAL_POSITION 596
#define LEN_PRO_TORQUE_ENABLE 1
: defines byte length for each items.
#define LEN_PRO_LED_RED 1
#define LEN_PRO_GOAL_POSITION 4
#define DXL1_ID 1
#define DXL2_ID 2
#define BAUDRATE 1000000
[Replace below codes to the DEFINES]
: defines addresses of the control table, which are used by Bulk Read and Write data.
#define PROTOCOL_VERSION 2.0
#define STOP_MOVING_MARGIN 20
Explanation
- BulkReadWrite : writes different data of two Dynamixels
#define ADDR_PRO_PRESENT_POSITION 611
#define LEN_PRO_PRESENT_POSITION 4
: The example uses DXL_ID #1 and DXL_ID #2 at 1M baudrate. It makes Protocol 2.0 packet and sends through the port ”/dev/ttyUSB0”. STOP_MOVING_MARGIN is for deciding whether the Dynamixel moves or not

## Slide 61: Examples
2. Demo & Codes
: dxl_error keeps the error got from Dynamixel. The index indicates the rotation direction of Dynamixel. The dxl_goal_position points out where the Dynamixel should be rotated to. dxl_goal_position shows the value of LED. The value of dxl_torque_ enable and dxl_torque_disable mean that torque ON and OFF, each. The dxl_goal_position will be allocated into param_goal_position byte array. The dxl_present_position1 and dxl_led_value_read2 store either of the present position and LED value of Dynamixels.
int dxl_goal_position[2] = {-150000, 150000};
UINT8_T dxl_torque_enable = 1;
UINT8_T dxl_torque_disable = 0;
UINT32_T dxl_present_position1 = 0;
UINT8_T param_goal_position[4];
int index = 0;
UINT8_T dxl_error = 0;
[Replace below codes to the VARIABLES]
: initialize the handlers of the port and the packet. Then initializes groupBulkWrite instance using two handlers above.
PortHandler *portHandler = (PortHandler*)PortHandler::GetPortHandler(DEVICE_NAME);
PacketHandler *packetHandler = PacketHandler::GetPacketHandler(PROTOCOL_VERSION);
[Replace below codes to the HANDLERS]
GroupBulkWrite groupBulkWrite(portHandler, packetHandler);
GroupBulkRead groupBulkRead(portHandler, packetHandler);
- BulkReadWrite : writes different data of two Dynamixels
UINT8_T dxl_led_value[2] = {0x00, 0xFF};
UINT8_T dxl_led_value_read2;

## Slide 62: Examples
groupBulkWrite.AddParam(DXL1_ID , ADDR_GOAL_POSITION, LEN_GOAL_POSITION, param_goal_position);
groupBulkWrite.AddParam(DXL2_ID , ADDR_LED_RED, LEN_LED_RED, led_value);
groupBulkWrite.TxPacket();
groupBulkWrite.ClearParam();
: AddParameter param_goal_position and led_value to groupBulkWrite parameter storage
: Transmits the packet
: ClearParameter of groupBulkWrite parameter storage.
param_goal_position[0] = DXL_LOBYTE(DXL_LOWORD(dxl_goal_position));
param_goal_position[1] = DXL_HIBYTE(DXL_LOWORD(dxl_goal_position));
param_goal_position[2] = DXL_LOBYTE(DXL_HIWORD(dxl_goal_position));
param_goal_position[3] = DXL_HIBYTE(DXL_HIWORD(dxl_goal_position));
: allocates dxl_goal_position into the byte array
2. Demo & Codes
- BulkReadWrite : writes different data of two Dynamixels
[Replace below codes to the BODY]
groupBulkRead.AddParam(DXL1_ID, ADDR_PRESENT_POSITION, LEN_PRESENT_POSITION);
groupBulkRead.AddParam(DXL2_ID, ADDR_LED_RED, LEN_LED_RED);
: AddParameter storage for Dynamixel’s present position and LED value
: enables the torque of the Dynamixel.
packetHandler->Write1ByteTxRx(portHandler, DXL_ID, ADDR_TORQUE_ENABLE, dxl_torque_enable, &dxl_error);

## Slide 63: Examples
groupBulkRead.TxRxPacket();
groupBulkRead.GetData(DXL1_ID, ADDR_PRESENT_POSITION, &dxl_present_position);
groupBulkRead.GetData(DXL2_ID, ADDR_LED_RED, &dxl_led_value_read);
: Transmits and receives the packet.
: GetData dxl_present_position or dxl_led_value_read from either of the Dynamixels
groupBulkRead.ClearParam();
: ClearParameter of groupBulkRead parameter storage.
2. Demo & Codes
- BulkReadWrite : writes different data of two Dynamixels
packetHandler->Write1ByteTxRx(portHandler, DXL_ID, ADDR_TORQUE_ENABLE, dxl_torque_disable, &dxl_error);
: disables the torque of the Dynamixel.

## Slide 64: Examples
2. Demo & Codes
- IndirectAddress : writes datas indirectly

## Slide 65: Examples
2. Demo & Codes
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_WRITE + 0, ADDR_GOAL_POS + 0, &dxl_error);
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_WRITE + 2, ADDR_GOAL_POS + 1, &dxl_error);
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_WRITE + 4, ADDR_GOAL_POS + 2, &dxl_error);
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_WRITE + 6, ADDR_GOAL_POS + 3, &dxl_error);
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_WRITE + 8, ADDR_LED_RED, &dxl_error);
: makes INDIRECTDATA replace 4 Byte GOAL_POSITION and 1 Byte LED_RED.
param_indirect_data_write[0] = DXL_LOBYTE(DXL_LOWORD(dxl_goal_position));
groupSyncWrite.AddParam(DXL_ID, param_indirect_data_write);
: AddParameter storage for the datas
param_indirect_data_write[1] = DXL_HIBYTE(DXL_LOWORD(dxl_goal_position));
param_indirect_data_write[2] = DXL_LOBYTE(DXL_HIWORD(dxl_goal_position));
param_indirect_data_write[3] = DXL_HIBYTE(DXL_HIWORD(dxl_goal_position));
param_indirect_data_write[4] = dxl_led_value;
: allocates dxl_goal_position and dxl_led_value into the byte array
GroupSyncWrite groupSyncWrite(portHandler, packetHandler, ADDR_INDIRECTDATA_WRITE, LEN_INDIRECTDATA_WRITE);
: initializes groupSyncWrite instance and points out the INDIRECTADDRESS.
- IndirectAddress : writes datas indirectly

## Slide 66: Examples
2. Demo & Codes
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_READ + 0, ADDR_PRES_POS + 0, &dxl_error);
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_READ + 2, ADDR_PRES_POS + 1, &dxl_error);
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_READ + 4, ADDR_PRES_POS + 2, &dxl_error);
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_READ + 6, ADDR_PRES_POS + 3, &dxl_error);
packetHandler->Write2ByteTxRx(portHandler, DXL_ID, ADDR_INDIRECTADDR_READ + 8, ADDR_MOVING, &dxl_error);
: makes INDIRECTDATA replace 4 Byte PRESENT_POSITION and 1 Byte MOVING.
GroupSyncRead groupSyncRead(portHandler, packetHandler, ADDR_INDIRECTADDR_READ, LEN_INDIRECTDATA_READ);
groupSyncRead.AddParam(DXL_ID);
groupSyncRead.GetData(DXL_ID, ADDR_INDIRECTDATA_READ, &dxl_present_position);
groupSyncRead.GetData(DXL_ID, ADDR_INDIRECTDATA_READ + 4, &dxl_moving);
: initializes groupSyncRead instance and points out the INDIRECTADDRESS.
: AddParameter storage for Dynamixel’s present position and LED value
: GetData of dxl_present_position and dxl_moving from the INDIRECTDATA
- IndirectAddress : writes datas indirectly

## Slide 67: Examples
2. Demo & Codes
- Reboot : makes the Dynamixel reboot

## Slide 68: Examples
2. Demo & Codes
packetHandler->Reboot(portHandler, DXL_ID, &dxl_error);
: Try to Reboot. DXL Green LED will flicker while it reboots
- Reboot : makes the Dynamixel reboot

## Slide 69: Examples
2. Demo & Codes
- FactoryReset : resets the Dynamixel by default
packetHandler->FactoryReset(portHandler, DXL_ID, OPERATION_MODE, &dxl_error);
: Try to FactoryReset. This will reset Dynamixel settings to default values
FactoryReset has three OPERATION_MODE :
0xFF : reset all values
0x01 : reset all values except ID
0x02 : reset all values except ID and baudrate

## Slide 70: SDK Structure

## Slide 71: SDK Structure
1. Folder
DynamixelSDK_vX.Y.zip
C++
C
(Developing)
PortHandler.cpp
Protocol1
PacketHandler.cpp
build
example
RobotisDef.h
Protocol2
PacketHandler.cpp
Protocol1
PacketHandler.h
Protocol2
PacketHandler.h
CPP
GroupBulkRead.cpp
GroupSyncRead.cpp
GroupBulkRead.h
GroupSyncRead.h
libdxl.so
Makefile
linux
win32
(Developing)
win64
(Developing)
Manual
GroupBulkWrite.cpp
GroupSyncWrite.cpp
GroupBulkWrite.h
GroupSyncWrite.h
PortHandlerLinux.cpp
PortHandlerLinux.h
include
src
.object
PortHandler.h
dynamixel_sdk
PacketHandler.cpp
dynamixel_sdk_linux
DynamixelSDK.h
dynamixel_sdk
dynamixel_sdk_linux
PacketHandler.h
dynamixel_sdk_windows
(Developing)
dynamixel_sdk_windows
(Developing)

## Slide 72: SDK Structure
2. Class
handles port and devices
handles port and devices with Linux
handles port and devices with Windows
handles packets
handles PROTOCOL 1.0 packets
handles PROTOCOL 2.0 packets
handles Dynamixel group for SyncRead
handles Dynamixel group for SyncWead
handles Dynamixel group for BulkWrite
PortHandler
PortHandlerLinux
PortHandlerWindows
PacketHandler
Protocol1PacketHandler
Protocol2PacketHandler
GroupSyncRead
GroupBulkWrite
GroupBulkRead
GroupSyncWrite
handles Dynamixel group for BulkRead

## Slide 73: SDK Structure
3. Methods
PortHandler
PortHandlerLinux
PortHandlerWindows
PacketHandler
Protocol1PacketHandler
Protocol2PacketHandler
GroupSyncRead
GroupBulkWrite
GroupBulkRead
GroupSyncWrite
OpenPort() | opens the port
ClosePort() | closes the port
ClearPort() | clears the port
SetPortName() | sets device name
GetPortName() | gets device name
SetBaudRate() | sets port baudrate
GetBaudRate() | gets port baudrate
GetBytesAvailable() | how many data can be read
ReadPort() | reads port packet buffer
WritePort() | writes port packet buffer
SetPacketTimeout() | sets time to decide communication result
IsPacketTimeout() | checks communication result

## Slide 74: SDK Structure
3. Methods
PortHandler
PortHandlerLinux
PortHandlerWindows
PacketHandler
Protocol1PacketHandler
Protocol2PacketHandler
GroupSyncRead
GroupBulkWrite
GroupBulkRead
GroupSyncWrite
TxPacket() | trasmits the packet
RxPacket() | receives the packet
TxRxPacket() | transmits & receives the packet
Ping() | ping
BroadcastPing | ping all connected Dynamixels
Action() | commands ‘Run’ the Regwritten
RegWrite() | writes the packets wait for the ‘Action’ command
Reboot() | Reboots Dynamixel
FactoryReset() | resets all Dynamixel settings
Read functions | functions for Reading
Write functions | functions for Writing
SyncRead functions | functions for SyncRead
SyncWrite functions | functions for SyncWrite
BulkRead functions | functions for BulkRead
BulkWrite functions | functions for BulkWrite

## Slide 75: SDK Structure
3. Methods
PortHandler
PortHandlerLinux
PortHandlerWindows
PacketHandler
Protocol1PacketHandler
Protocol2PacketHandler
GroupSyncRead
GroupBulkWrite
GroupBulkRead
GroupSyncWrite
AddParam() | adds parameter to the packet
RemoveParam() | removes parameter to the packet
ClearParam() | clears parameter to the packet
TxPacket() | transmits the packet
RxPacket() | receives the packet
TxRxPacket() | transmits & receives the packet
GetData() | gets read data

## Slide 76: SDK Structure
3. Methods
PortHandler
PortHandlerLinux
PortHandlerWindows
PacketHandler
Protocol1PacketHandler
Protocol2PacketHandler
GroupSyncRead
GroupBulkWrite
GroupBulkRead
GroupSyncWrite
AddParam() | adds parameter to the packet
ChangeParam() | removes parameter to the packet
ChangeParam() | changes parameter of the packet
ClearParam() | clears parameter of the packet
TxPacket() | transmits the packet

## Slide 77: Information
For the details, please visit ROBOTIS support page
: support.robotis.com/en/